## Slide 1: Robot Forward/Inverse Kinematics
Notes: Hello Thank you for inviting me first.
I hope Hanwha and Schaeffler can help each other.
I will briefly introduce myself.
I am Bae Gang-tae, research engineer at Hanwha Precision Machinery Robot Division.
As you have seen at the last meeting in korea,
this is the leader engineer Mr lee in the algorithm part
Today we will go over what we need to worry about

## Slide 2: Kinematic Chain
DH(Denavit-Hartenberg) parameters
Transformation matrix
: joint angle – the angle between the axes about the axis
: link offset – the distance from the origin of frame {i-1} to axes along the axis
: link length – the distance between the and axes along the axis
: link twist – the angle from the to axis about axis
The transformation from {i-1} to {i} :

## Slide 3: A-2-Link Robot(SE(2))
Forward kinematics
DH parameters
Inverse kinematics
Solve “two” nonlinear equations in “two” unknowns.
Inverse Kinematics for a 2-Joint Robot Arm Using Geometry | Robot Academy
Analyzing a 2-joint planar robot arm | Robot Academy
Link |  |  |  | 
1 |  | 0 | 1 | 0
2 |  | 0 | 1 | 0
Link |  |  |  | 
1 |  | 0 | 1 | 0
2 |  | 0 | 1 | 0

## Slide 4: Hanwha Collaborative Robot
HCR12
HCR5

## Slide 5: Inverse kinematics – Numerical Solution
Newton’s method
Line search method
AME 50551 – Introduction To Robotics – Patrick M. Wensing (nd.edu)
Root finding :
Newton’s method for inverse kinematics :
(geometric) Jacobian
Step size selection : Armijo’s backtracking line search method

## Slide 6: Project 1
AME 50551 – Introduction To Robotics – Patrick M. Wensing (nd.edu)

## Slide 7: 별첨. Kinematic Calibration
Course material Robotics 2 (uniroma1.it)
HCR’s Improvement by kinematic calibration
Accuracy and repeatability
Numerical inverse kinematic solution [6]
Before calibration
After calibration
1.3~2.2 mm
≤ 0.4 mm

## Slide 8: References
Spong, M. W., Hutchinson, S., & Vidyasagar, M. (2020). Robot modeling and control. John Wiley & Sons.
Corke, P. I., Jachimczyk, W., & Pillat, R. (2011). Robotics, vision and control: fundamental algorithms in MATLAB (Vol. 73, p. 2). Berlin: Springer.
Srinivasan, M. (2015). Mechanics and Control of Robots
Wensing, P. M. (2017). Introduction to Robotics-Lecture 20: Numerical Inverse Kinematics
De Luca, A. (2023). Robotics2Introduction to Robotics-Lecture 01: Calibration
Nubiola, A., & Bonev, I. A. (2014). Geometric approach to solving the inverse displacement problem of calibrated decoupled 6R serial robots. Transactions of the Canadian Society for Mechanical Engineering, 38(1), 31-44.

## Slide 9: Thank you
Notes: appreciate for listening
Anything else question?